## Slide 1
New parallel architectures for
medical simulation
Hadrien Courtecuisse

## Slide 2: Medical Simulations
New technologies :
  Mini-invasive surgery, interventional radiology
  Interface the surgeon and the patient
  Video control, no haptic sensations
Create a virtual representation of the patient :
  Give a bio-mechanical behavior
Surgery : complex practice
  Require a long training
  Involve many risks
Reproduce a similar surgical fields

## Slide 3: Medical Simulations
Sim
Learning
Assistance
Planning
Simulation for training :
  Decrease the learning time
  Improve training
Pacification of a complex surgery :
  Evaluation of the best strategy
  Select the equipment best suited
  Simulations patient-specific
Assistance during the operation :
  Give more information to surgeons
  Decrease risks of the operation
Computation time constraints
Precision

## Slide 4: Interactive Simulations
Deformation
Collision detection
Contact resolution
Rendering
User action
Simulation loop
Interactive simulation :
  Fast computation
  Human interaction
Several steps :
  Computation of the deformation
  Collision detection
  Contact resolution
  Rendering of the simulation
All must be done 25 times per second
Human interaction :
  Use stable algorithms
  Unpredictable motion
  Haptic device

## Slide 5: Contributions
GPU parallelization of implicit integrator
Asynchronous preconditioning
Deformation
Collision detection
Contact resolution
Rendering
Collision detection on GPU
Extension to volume constraints
Gauss-Seidel parallelization
GPU computation of the compliance for beam model
GPU computation of the compliance based on the preconditioner

## Slide 6
1
5
4
2
3

## Slide 7: Equations formulation
Continuum mechanics
  Assumption of continuity of matter
  Based on physics law
  Define a deformation model
Resolution based on finite element method
  Discretization in small elements
  Integrate and solve equations by elements
  Approximation which depends on the size of elements
Constitutive law
Resolution of a dynamic system :
  Time evolution of deformable bodies
  Involves acceleration, velocity, and position
Any deformation model describe a relation such as :
Strain
Stress

## Slide 8: Interactive deformation model
Small displacements and small deformations :
  Linear constitutive law
  Simple and fast
  Inflates for large deformations/displacements
Large displacements and small deformations :
  Compensate geometrical non linearity
  Take into account the rotations / linear deformation
  Co-rotationnal model
Large displacements and large deformations :
  Simulation of large deformation
  Hyperelastic model :
  MJED [Marchesseau et al. 2010]
  TLED [Comas et al. 2008]
  Difficult to solve in real time

## Slide 9: Temporal system evolution
Explicit integration :
  Local resolution
  Fast and parallelizable
  Stability implies to use very small time steps
  Implicit integration :
  Update the acceleration from position and velocity at the end of the time step
  Stable with large time steps
  Rearranging equations gives the linear system :
  Linearization of around the initial position [Baraff et al. 1998]
Problem 1 : How to solve in real time ?

## Slide 10: Collision detection
Collision detection :
  Find primitives in intersection or close to intersection
Many different methods [Teschner et al. 2005]
  Bounding volume hierarchy
  Distance field
  GPU based methods
Medical simulation implies :
  Handle Complex geometries and deformable objects
  Handle topological modifications (cutting)
  Handle self-collisions
  Handle friction/grasping
  Keep simple formulation for the response
Problem 2 : How to detect collisions in real time ?

## Slide 11: Collision response
with
Signorini law to build a LCP (Linear Complementary Problem)
Problem 3 : How to handle mechanical coupling in real time ?
  Solved with a Gauss-Seidel method [Courtecuisse et al., HPCC 2009]
  Find which solves interactions
dt=0,01
Compliance

## Slide 12: Previous solutions
Compliance Warping [Saupin et al. 2008]
1500 elements
Only the liver is simulated
Response based on pre-computations
Simplified model
Objectives :
Increase the number of elements
Add other organs
Handle cutting
Better mechanical coupling
Real time constraints

## Slide 13: New parallel architectures
Parallelization of a simulation is not a new idea :
  Parallel processors, distributed processors, …
Real time simulation constraints :
  A lot of very fast computations
Difficult to increase the frequency of processors
  Parallelization of algorithms
Use GPU to achieve computations (GPGPU).

## Slide 14: GPU architecture
GPU is seen as a specialized co-processeur :
  Achieve high parallel tasks
CPU
Kernel 1
GPU
Grille 1
Block
(0,0)
Block
(1,0)
Blobk
(2,0)
Block
(0,1)
Block
(1,1)
Block
(1,2)
Grille 2
Kernel 2
Block (1,1)
Thread
(0,0)
Thread
(1,0)
Thread
(2,0)
Thread
(3,0)
Thread
(4,0)
Thread
(0,1)
Thread
(1,1)
Thread
(2,1)
Thread
(3,1)
Thread
(4,1)
Thread
(0,2)
Thread
(1,2)
Thread
(2,2)
Thread
(3,2)
Thread
(4,3)
Two level of parallelism :
  A Grid contains several blocs
  A Block contains several threads
GPU Parallelization strategies are very different than CPU parallelization :
  Run thousand of threads to exploit efficiently the GPU
GPU programing :
  Local synchronisations very fast
  Global synchronisations very slow (Synchronisation with the CPU)

## Slide 15
1
5
4
2
3
Deformation
Collision detection
Contacts resolution
Simulation rendering
GPU parallelization of implicit integrator
Asynchronous preconditioning

## Slide 16: Solving methods
Pre-compute the inverse of the system :
  Actually compute such as
  Benefits: Fast
  Disadvantages: Limited to linear and to coarse models [Cotin et al. 96]
Compute a factorization :
  or (Cholesky factorization)
  Benefits: Stable and accurate, sparse factorization can be applied for detailed meshes
  Disadvantages: Time to factorize is important
Use an iterative algorithm :
  Conjugate Gradient algorithm (CG) [Baraff et al. 1998]
  Benefits: Possible to stop computations as soon as the desired precision is achieved
  Disadvantages: Convergence problems
Problem 1 : How to solve in real time ?

## Slide 17: GPU-based implicit integration
  Parallelization of implicit integration [Allard et al. 2011, GPU Gems]
Only and are not linear algebra operations
  Accumulate forces on each DOF
Force
dForce
Only two scalar and must be transferred between CPU and GPU to check convergence
Most of operations and are linear algebra operations
  Parallelization solutions exists
+
dot
GPU
CPU

## Slide 18: Implicite solver on GPU
Accumulate forces on each points
  Independent of the deformation model
  Dependences between edges
Parallelization methods :
  Graph partitioning [Hermann et al. 2010]
  Small number of processors
  Graph coloration [PhysX, Bullet]
  Graph very sparse, analysis of the graph
Treat each DOF in parallel
  Assign an unique ID to each edge
  Pre-compute neighbourhood associations
  Require one global synchronisation
Vecteur pré-calculé :
Synchronisation
Kernel2
0
1
2
3
4
Vecteur temporaire :
Kernel1

## Slide 19: Performances evaluation
Nombre
Speedup between 5 to 25
Simulate 300 000 elements in real time (CG limited to 25 iterations)
Number of elements
Speedup

## Slide 20: Asynchronous preconditioner
High number of iterations for ill conditioned problems
  Non homogeneous objects
  Non uniform meshes

## Slide 21: Asynchronous preconditioner
Number of iterations
Computation time (ms)

## Slide 22: Asynchronous preconditioner
Fast convergence with additional overheads
  Overhead to inverse the preconditioner
  Overhead to apply the preconditioner at each iteration
Use a preconditioner :
  Approximation of the system which is easier to invert
S
New FEM Computation
CG
Iterations
Precond
Application
Precond
Computation
High number of iterations for ill conditioned problems
  Non homogeneous objects
  Non uniform meshes

## Slide 23: Asynchronous preconditioner
Number of iterations
Computation time (ms)

## Slide 24: Asynchronous preconditioner
Fast convergence with additional overheads
  Overhead to inverse the preconditioner
  Overhead to apply the preconditioner at each iteration
Exploit time coherency between time steps
Use a preconditioner :
  Approximation of the system which is easier to invert
S
New FEM Computation
CG
Iterations
Precond
Application
Precond
Computation
High number of iterations for ill conditioned problems
  Non homogeneous objects
  Non uniform meshes

## Slide 25: Asynchronous preconditioner
Number of iterations
Computation time (ms)

## Slide 26: Asynchronous preconditioner
Fast convergence with additional overheads
  Overhead to inverse the preconditioner
  Overhead to apply the preconditioner at each iteration
Exploit time coherency between time steps
Use a preconditioner :
  Approximation of the system which is easier to invert
S
New FEM Computation
CG
Iterations
Precond
Application
Precond
Computation
Synchronization
High number of iterations for ill conditioned problems
  Non homogeneous objects
  Non uniform meshes

## Slide 27: Asynchronous preconditioner
Simulation
Step
Notification
Notification
Notification
Enable to use advanced preconditioners :
  Use an exact factorization of the system
  remains sparse and can be applied to detailed meshes
Update the preconditioner periodically [Courtecuisse et al. 2010, Vriphys]
Simulation
Step
Simulation
Step
Simulation
Step
Simulation
Step
Simulation
Step
Simulation
Step
Simulation
Step
Simulation
Step
Simulation
Step
Simulation
Step
Simulation
Step
Synchronization
Synchronization
Synchronization

## Slide 28: Asynchronous preconditioner
Computation time (ms)
Number of iterations

## Slide 29: Asynchronous preconditioner
We can compute rotations independently of the deformation model :
  For co-rotational model we use directly the rotations computed by the model
  For other models we use shape matching method [Müller et al. 2005]
Heuristic to limit the divergence of the préconditionneur :
  Apply rotation which appears since the last update of the preconditioner
  Limit the effect of geometrical non linearities

## Slide 30: Asynchronous preconditioner
Number of iterations
Computation time (ms)

## Slide 31: Asynchronous preconditioner
We can compute rotations independently of the deformation model :
  For co-rotational model we use directly the rotations computed by the model
  For other models we use shape matching method [Müller et al. 2005]
Only few time steps of simulation are necessary to update the preconditioner.
Heuristic to limit the divergence of the préconditionneur :
  Apply rotation which appears since the last update of the preconditioner
  Limit the effect of geometrical non linearities

## Slide 32: Asynchronous preconditioner
Number of iterations
Computation time (ms)

## Slide 33
1
5
4
2
3
Deformation
Collision detection
Contacts resolution
Simulation rendering
Collision detection on GPU
Extension to volume constraints

## Slide 34: Triangles rasterization
LDI
Depth map of the objects
  Sorted list of the intersections
Extension of [Faure et al. 2008]
LDI Computation (Layer Depth Images)
  2D Images discretized in pixel
  Size of the pixels define the precision

## Slide 35: Rastérisation volumique
  3 LDI in orthogonal directions gives a 3D representation of the objects
  OpenGL rendering
  Collisions detection
Intersection volumes :
  1 volume by pair of intersection
Gradients of the volume
  Sum unitary gradients over each pixel

## Slide 36: Triangles rasterization
LDI
Initial mesh
2
Projection des triangles
Upper and lower line, Zmean, α, β,...
Lmax
Lmin
L1
1
0
Liste les cellules par triangles
Triangles → Cells
Rastérisation
LDI
Tri par (cellules,z)
Cells→ Triangles
LDI
Project triangles
List cells by triangles
Rasterization
Sort
(cells,z)

## Slide 37: Volume constraints
Transform Signorini in volume [Allard et al. 2010, Siggraph]
  Associate a small area around one contact
  Only one lagrangian multiplier on this area
  We compute the necessary pressure to solve the contact
Friction support :
  Compute an average frame around the contact to express friction

## Slide 38: Parameter for accuracy
Separate volumes:
  Groups of pixels
  Take into account local variations
  Independent from the topology
Compromise accuracy/computation time
  Easy to control
One constraint per intersection
  Fast
  Cannot simulate local variations

## Slide 39: Results
20 deformable Torus falling[Irving et al 2007]
  GPU implicit integration
  90k tetrahedra elements
  97k collision triangles
12.4 FPS on a Nvidia Geforce GTX 580
  Rasterization LDI: 5 ms
  Contacts modelisation: 4 ms
  FEM Solver: 71 ms

## Slide 40: Avantages de la méthode
Enable real time computation
  Large number of triangles
Choose accuracy :
  Size of pixels, size of grid
  Independent from the geometry
  Keep a small number of constraints
Robust and accurate :
  Handle large intersections at initial step
  Handle friction
  Handle self-collision without important overhead
  Simulate data from patient-specific segmentation
Handle topological modifications:
  No pre-computations
Limitations :
  Only for volume objects
  Can not anticipate collisions

## Slide 41
1
5
4
2
3
Deformation
Collision detection
Contacts resolution
Simulation rendering
Gauss-Seidel parallelization
GPU computation of the compliance for beam model
GPU computation of the compliance based on the preconditioner

## Slide 42: Computation of the compliance
Problem 3 : How to solve in real time?
avec
is the jacobian of contacts (sparse)
is a measure of the interpenetration
λ is the contact force
is the compliance matrix
dt=0,01
dt=0,001
dt=0,0001
Not real time
dt=0,01
Compliance
Warping
Consider only the diagonal
Compliance Warping [Saupin et al. 2008]
  Pre-compute the inverse of the system
  Warping to limit geometrical non linarites
Exploit the characteristics of the model:
  [Courtecuisse et al. 2009, PBMB]

## Slide 43: Preconditioners for contacts
Reuse the préconditionneur to solve contacts [Courtecuisse et al. 2011, MICCAI]
However, we don’t have but it’s factorization
  We know how to apply the preconditionneur :
LDL
  We repeat this operation until we get
  Finally we get the compliance matrix with:
Compliance
  ( est creuse)
The Compliance matrix is only a scaled version of the inverse of the system

## Slide 44: GPU parallelization
GPU
Multiprocessor
Multiprocessor
Multiprocessor
Multiprocessor
Multiprocessor
Multiprocessor
LDL
S
Each resolution is computed by a single multiprocessor
A second level of parallelism is used inside each resolution
  Well suit to GPU architectures
  Only use local synchronisations
LDL
S
LDL
S
LDL
S
LDL
S
LDL
S
The most time consumming task is the compuation of
Each column can be computed in parallel
Thread
(0,0)
Thread
(0,1)
Thread
(1,0)
Thread
(1,1)
Thread
(2,0)
Thread
(2,0)

## Slide 45: Validation of the method
dt=0,01
Update every 3 time steps on average
Compare the positions with different approximations of the Compliance
  The green shape represent the exact solution
  The object is non homogeneous : Red tetrahedra are stiffer than blue ones
With Asynchronous update of the preconditioner, we get almost the correct solution
  The green part and the blue part overlap perfectly
dt=0,01
Compliance
Warping
dt=0,01
Update every 50 time steps
dt=0,01
Update every 20 time steps

## Slide 46: Computation time on GPU
Accélération
Temps (sec)
Nombre de Contraintes
Nombre de Contraintes
With GPU implementation we can solve up to 128 constraints at the same cost
  Real time computation is very limited on CPU (less than 10 constraints)
  Enable to handle large number of contacts in real time on GPU
This method is well suit with LDI approach

## Slide 47: Advantages of the method
Enable to take into account the correct mechanical coupling between contacts
  GPU implementation enable to achieve real time performances
  Well suit to the collision detection by rasterization
Automatically handle topological changes:
  Without an important overhead
  Currently limited to carving (constant number of DOF)
  Non stable dring the cutting.
Can be used with non linear models:
  Preliminary test on hyperelasitc models (MJED)
  Haptic with non linear models
  Non stable when element are inverted

## Slide 48
1
5
4
2
3

## Slide 49: Résection hépatique
We generate different models from the surface
We use meshes from a CT segmentation
  Reproduce patient specific simulations
  Automatic 3D segmentation method [IRCAD]

## Slide 51: Chirurgie de la cataracte
Lens opaque
Cataract operation :
  Opacification of the lens
  Prevent the passage of the light
Treatment :
  Surgical procedure to remove the disease lens

## Slide 53
Conclusion

## Slide 54: Travaux futurs
Contributions at different level :
  Algorithms parallelization
  New algorithms based on GPU
Improve precision of simulation in real time
  Produce realistic medical simulations
  Toward using the simulation during the surgery
Short term :
  Use new preconditioners
  Extension of LDI to a continuous collision detection
  Make algorithms robust against topological modifications
Long term :
  Validation of the deformation of the organs (error evaluation)
  Creation automatic of medical simulations

## Slide 55
Thank you for your attention